## Slide 1: ISOP: Machine Learning-Assisted Inverse Stack-Up Optimization for Advanced Package Design
Hyunsu Chae1, Bhyrav Mutnury3, Keren Zhu1, Douglas Wallace3, Douglas Winterberg3, Daniel de Araujo4
Jay Reddy3, Adam Klivans2 and David Z. Pan1
1ECE Department, The University of Texas at Austin
2CS Department, The University of Texas at Austin
3Dell Infrastructure Solutions Group
4Electronic Board Systems, Siemens EDA
This work is supported in part by NSF under grants 1718570, 2019844, and 2112665, and by the NSF AI Institute for Foundations of Machine Learning (IFML).

## Slide 2: Outline
Motivation
Problem formulation
ISOP framework
Experimental results
Conclusion

## Slide 3: Advanced Package Design and PCB trend
High Density Interconnect (HDI) PCB Market forecast
https://www.researchandmarkets.com/reports/5682545
CAGR 6.1%
Motivation
Problem Formulation
ISOP
Results
Conclusion
Growing demand for
low loss and high-speed HDI PCBs
Main goal of PCB design is to ensure
component connectivity and communication

## Slide 4: PCB Stack-Up Design Challenges
PCB Stack-up
  15+ parameters, big solution space
  Different system and technology requires different specifications
  Uses computationally expensive EM (electromagnetic) simulations
Problem Formulation
ISOP
Results
Conclusion
Motivation
   Done manually  time-consuming, tedious and sub-optimal

## Slide 5: Inverse Stack-Up Design Task
What is the optimal stack-up design?
Motivation
Problem Formulation
ISOP
Results
Conclusion
Parameters | LB-UB | Step
 | 2-5 | 0.1
 | 2-10 | 0.5
… | … | …
 | 0.001-0.02 | 0.001
Parameters | LB-UB | Step
 | 2-5 | 0.1
 | 2-10 | 0.5
… | … | …
 | 0.001-0.02 | 0.001

## Slide 6: ISOP Framework
ISOP leverages:
1) Hyper-parameter optimization process
2) ML surrogate model
3) Efficient objective function
ISOP could be extended to other scenarios of interconnect optimization
Motivation
Problem Formulation
ISOP
Results
Conclusion

## Slide 7: ISOP Framework
Overall flow
Motivation
Problem Formulation
Results
Conclusion
ISOP
Non-convex search space
Discrete HPO algorithm
(Harmonica)
Runtime overhead
ML surrogate model
Multiple different objectives
Efficient objective function

## Slide 8: HPO algorithm
Harmonica algorithm
  Discrete domain HPO
→ avoid explorations with invalid design parameters
  Parallelized design parameter sampling
→ fast and efficient batched evaluation of samples
Motivation
Problem Formulation
Results
Conclusion
ISOP

## Slide 9: ML Surrogate Model
ML surrogate model replaces expensive EM simulations
  Fast query of evaluation metrics -> observe more samples in large search space with reduced runtime
Motivation
Problem Formulation
Results
Conclusion
ISOP
Regression problem with tabular features
  90k unique stack-up designs
  Preprocessing
  One model for each objectives
  MAPE/sMAPE

## Slide 10
Optimization objective functions
Ultimate objective function (non-differentiable) | Smooth objective function Enables more searches at the border
Used for later roll-out stage, with actual simulation | Used for search stage, with ML surrogate model
Ultimate objective function (non-differentiable) | Smooth objective function Enables more searches at the border
Used for later roll-out stage, with actual simulation | Used for search stage, with ML surrogate model
Motivation
Problem Formulation
Results
Conclusion
ISOP

## Slide 11: Experiment Setting
ML Training Dataset Space
Motivation
Problem Formulation
ISOP
Results
Conclusion
Experiment Tasks
Experiment Search Space
>
>

## Slide 12: Experiments: ISOP vs Baseline
Under similar runtime
Motivation
Problem Formulation
ISOP
Conclusion
Results
Under similar samples seen
Success rate | T1 | T2 | T3 | T4
SA-1 | 1 | 1 | 0.1 | 0.1
BO-1 | 1 | 1 | 1 | 1
ISOP | 1 | 1 | 1 | 1
Chart: Task
| T1 | T2 | T3 | T4
SA-1 | 0.4512 | 0.4725 | 2.054 | 0.993
BO-1 | 0.498 | 0.7424 | 0.5852 | 0.6
ISOP | 0.4403 | 0.4605 | 0.4623 | 0.4502
Chart: Task
| T1 | T2 | T3 | T4
SA-2 | 0.4576 | 0.4693 | 1.1065 | 1.067
BO-2 | 0.4733 | 0.5852 | 0.5436 | 0.5186
ISOP | 0.4403 | 0.4605 | 0.4623 | 0.4502
14.95%
13.20%
2.41%
21.00%
24.97%
2.54%
3.78%
1.86%
Success rate | T1 | T2 | T3 | T4
SA-2 | 1 | 1 | 0.2 | 0.1
BO-2 | 1 | 1 | 1 | 1
ISOP | 1 | 1 | 1 | 1

## Slide 13: Experiments: ML surrogate model accuracy
Evaluation of trained models
Motivation
Problem Formulation
ISOP
Conclusion
Results
Predicted performance verses ground truth

## Slide 14: Experiments: Case Study
Motivation
Problem Formulation
ISOP
Conclusion
Results
Example of output
  The advantages of our flexible framework will continue to expand to enable global optimization over different performance metrics

## Slide 15: Conclusion
ISOP offers agile HDI PCB stack-up design framework, automating the process and producing excellent results in minutes.
Inverse stack-up optimization is formulated as an HPO problem, and accelerated with efficient ML surrogate model and objective function.
ISOP reduces design cycle time from hours to minutes and outperforms baseline methods, as demonstrated in experiments.
ISOP can be extended to other interconnect optimization scenarios.
Motivation
Problem Formulation
ISOP
Results
Conclusion

## Slide 16: Thank You