## Slide 1: PulseRF: Physics-Augmented ML Modeling and Synthesis for High-Frequency RFIC Design
Hyunsu Chae, Hao Yu, Sensen Li, and David Z. Pan
ECE Department, The University of Texas at Austin

## Slide 2
Outline
Motivation
Problem Formulation
PulseRF Framework
Experimental Results
Summary

## Slide 3: RFIC (Radio Frequency Integrated Circuit)
RFIC components are fundamental in wireless systems
RFIC = active + passive components
Motivation
[Behzad Razavi, RF Microelectronics]
Active Components
Passive Components

## Slide 4: RFIC Passive Design Challenges
Motivation
The majority of RFIC design efforts are focused on passive design and optimization
  Occupy most of core chip area
  Need to balance many different design objectives
    Minimize loss
    Maximize bandwidth
    Address impedance transformation and mismatch, ..
  Have multiple functions
    Facilitate facilitating output, inter-stage, and input matching
    Filtering
    Phase-shifting, ..

## Slide 5: RFIC Passive Design Challenges
Optimization is confined to a limited set of topology templates
Slow simulation restricts the number of optimization iterations possible
More general definition of design space
Physics-augmented ML model for fast design evaluation
Bayesian optimization-based design synthesis for efficient exploration of design space
Motivation

## Slide 6: PulseRF Problem Formulation
Low Loss Impedance Transformation
  The major function of RF passive networks is to achieve impedance transformation with minimal loss
Problem Formulation

## Slide 7: PulseRF Problem Formulation
Given target specifications
  design space
  load impedances ,
  output impedances ,
  passive efficiency
Solve for
  design layout
Problem Formulation

## Slide 8: 1) Design Space Formulation
  Pixelated approach : randomly scattered pixels and isolated shapes lead to redundant design performance [1][2]
Why do we need good design space?
PulseRF Methods
Conventional
Template-based
Complete
Pixelated
PulseRF
  Conventional approach : highly-restricted, few design choices
  [1] E. A. Karahan, Z. Liu and K. Sengupta, "Deep-Learning-Based Inverse-Designed Millimeter-Wave Passives and Power Amplifiers," JSSC 2023
  [2] J. Lee, W. Jia, B. S. -. Rodriguez and J. S. Walling, "Pixelated RF: Random Metasurface Based Electromagnetic Filters," NEWCAS 2023
  Meaningful designs and not too restricted design space

## Slide 9: 1) Design Space Formulation
⇨ PulseRF: Flexible template-based approach with local deformations
40x40 grid (120 um x 120um), multiple layers, ring structure
PulseRF Methods
28 parameters
Local deformations
Diverse ring shapes

## Slide 10: 2) ML Surrogate Model
Why do we need surrogate ML model?
  Fast evaluation of design (EM simulation is slow) in optimization flow
  The model can be repeatedly used to address various design goals in RF passive design
ML Surrogate
Model
 | S11 | S12 | S13 | S14 | S33 | S34
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
… |  |  |  |  |  | 
300 |  |  |  |  |  | 
Layout Image
S-parameters
PulseRF Methods

## Slide 11: 2) ML Surrogate Model
3D-to-2D UNet
  Similar input/output dimension
  Able to capture both localized and contextual features
  Adapt UNet to handle 3D (image)-to-2D (S-parameters)
PulseRF Methods

## Slide 12: 2) ML Surrogate Model
[3] Hakki Mert Torun et al, Causal and passive parameterization of s-parameters using neural networks, MTT 2020.
Enforce physics into the model
  Causality enforcement layer (CEL) [3]
    Utilizing the enate relationship of real and imaginary parts of S-parameters
  Kramer-Kronig compensation layer (KKCL)
    Alleviate the discretization error at higher frequency range
PulseRF Methods

## Slide 13: 3) Inverse Design
Bayesian optimization-based framework
  Large design space ()
  Leverage Bayesian optimization’s ability for efficient selection of new samples
  Not relying on the quantity and quality of the initial design samples
  Expected improvement (EI) as acquisition function
  Tree-structured Parzen estimator (TPE)-based modeling
PulseRF Methods

## Slide 14: 3) Inverse Design
Considering local deformation as noise in the optimization
  Instead of considering them as design parameters
PulseRF Methods
Cost function
  Weighted sum of each objective with frequency weight

## Slide 15: Evaluation of ML Surrogate Model
ML model reduces design evaluation time to milliseconds
Chart: 
| R2 score
STCNN+CEL[1] | 0.724
CNN+CEL | 0.807
UNet+CEL | 0.929
Proposed (UNet+CEL+KKCL) | 0.941
Chart: 
| MSE_f
STCNN+CEL[1] | 0.082
CNN+CEL | 0.064
UNet+CEL | 0.031
Proposed (UNet+CEL+KKCL) | 0.03
R2 score
(Bigger the better)
MSE_f
(Smaller the better)
NMSE_f
(Smaller the better)
Chart: 
| NMSE_f
STCNN+CEL[1] | 0.261
CNN+CEL | 0.165
UNet+CEL | 0.069
Proposed (UNet+CEL+KKCL) | 0.068
STCNN+CEL [3]
CNN+CEL
UNet+CEL
Proposed (UNet+CEL+KKCL)
Results
15

## Slide 16: Evaluation of Inverse Design Method
Experimental setting: reflect practical design requirements
  Differential-to-differential (D-D) transformation
  Single-ended-to-differential(SE-D) transformation
  Each with (realreal, complexreal, complexcomplex) tasks
HFSS simulation (High-Frequency Structure Simulator)
Teledyne InP 250nm HBT
Results

## Slide 17: Evaluation of Inverse Design Method
Observe the effect of local deformation (bumps)
Results
Chart: D-D Tasks FoM (lower the better)
| T1 | T2 | T3
No bumps | 51.5 | 159 | 229.3
Bumps | 25.3 | 40.7 | 122.5
Chart: SE-D Tasks FoM (lower the better)
| T1 | T2 | T3
No bumps | 2849.6 | 1751.7 | 618.3
Bumps | 2759.6 | 433.7 | 244.4
PulseRF
without deformations
PulseRF
with deformations
Comparison for genetic algorithm vs PulseRF (BO-based)
Chart: D-D Tasks FoM (lower the better)
| T1 | T2 | T3
GA | 95.59 | 74.82 | 392.42
PulseRF | 25.28 | 32.79 | 122.46
Chart: D-SE Tasks FoM (lower the better)
| T1 | T2 | T3
GA | 3878.6 | 695.9 | 188.7
PulseRF | 2759.6 | 358 | 244.4
GA
PulseRF

## Slide 18: Comparison with Expert Manual Design
PulseRF
  Speed-up
  Better performance
  Non-intuitive and incomprehensible design
Results
Re[Zp] = Re[Zn]
Im[Zp] = Im[Zn]

## Slide 19: Summary
PulseRF framework:
  Provides ML-assisted tool for automating RF passive design synthesis for generic multi-layer, multi-port structures
  Utilizes the physics-augmented ML model that accurately predicts S-parameter up to 300GHz
  Achieves faster, high-quality designs that is not intuitive by human
Summary

## Slide 20: Thank You!