## Slide 1: ML-Assisted RFIC Design Enablement: The New Frontier of AI for EDA
Hyunsu Chae1, Song Hang Chai1, Taiyun Chi2, Sensen Li1, and David Z. Pan1
1University of Texas at Austin, Austin, Texas, USA
2Rice University, Houston, Texas, USA
1
ASPDAC 2025: Invited paper
Notes: Presenting on behalf of Prof David Pan

## Slide 2: RFIC (Radio Frequency Integrated Circuit)
RFIC components are fundamental in wireless systems
RFIC = active + passive components
[Behzad Razavi, RF Microelectronics]
Active Components
Passive Components
Notes: RFICs are essential in our daily lives, powering the wireless systems in devices from smartphones and WiFi routers to satellite communication and radar.
RF circuit design can be divided into two objectives, active component design and passive component design.

## Slide 3: RFIC = Active + Passive
Active-Passive interactions influence the overall RFIC performance
Active Components
Passive Components
Provides the essential power and gain
Signal generation, amplification,…
Define the frequency response
Impedance matching, filtering, phase shifting, stabilization, harmonic manipulation,…
C
The majority of RFIC design efforts are focused on passive design and optimization
Notes: This interaction between the active and passive component influence the overall RFIC performance.
Currently, the majority of RFIC design efforts are focused on passive design and optimization and this will be our focus in today’s talk.

## Slide 4: RFIC Passive Design Challenges
Need to balance different design objectives across frequencies
  Minimize loss, maximize bandwidth, address impedance transformation
Follows active component design and can limit their performance
Occupy most of chip area
  e.g., the passive component in an RF power amplifier (PA) occupies over 80% of the core chip area
[Li+, JSSC’24]
[Zhang+, TMTT’23]
[Zhang+, JSSC’23]
Actives
Notes: The RFIC passive components have distinctive nature as it not only transfer signals but also handle high-frequency demands. ( It need to handle parasitic effects, electromagnetic interference (EMI), signal integrity (SI), and other non-idealities. )

## Slide 5: RFIC Passive Design Flow
Computationally expensive simulations
Iterative
Heuristically-constrained
High entry barriers for new designers
Fast evaluation utilizing ML models
Automated
Non-intuitive and beyond human
Lowered entry barriers for new designers
Notes: In this presentation, we will review recent advancements in two key components of the ML-assisted design flow: ML-surrogate models and optimization methods.

## Slide 6: RFIC Passive Design Flow
Computationally expensive simulations
Iterative
Heuristically-constrained
High entry barriers for new designers
Fast evaluation utilizing ML models
Automated
Non-intuitive and beyond human
Lowered entry barriers for new designers
Notes: First we will go over the ML surrogate modeling.

## Slide 7: ML Surrogate Modeling
Replace EM simulation with ML surrogate models for faster performance evaluation
EM simulation is the major bottleneck of RF manual design
  Solves Maxwell’s equations with 3D mesh
RF
Passive
Designs
S-parameters
ML Surrogate Model
Passive Designs
Notes: EM simulation is the major bottleneck of RF manual design.
Conventional EM solver, such as Ansys HFSS employs numerical methods to solve Maxwell’s equations.
As the complexity of the design grows, so do the memory and computation demands due to the iteration required for convergence.

## Slide 8: ML Surrogate Modeling
S-parameters (Scattering parameters)
  Describes the electrical behavior of a multi-port network
Limited research on ML surrogate modeling for RF passive designs..
Include reviews of related works in package design
    Characterizes the voltage (power) being transferred between ports
  Matrix of complex numbers over frequency
  Can be converted to Z, Y-parameters or other metrics to analyze various characteristics
Notes: To quickly review what is Scattering Parameters…
We include reviews of related works in package design for predicting S-parameters in general.

## Slide 9: ML Surrogate Modeling
Categorize based on different representations
Tabular (or Template) Based ML Modeling
  EM structures are represented using predefined templates and parameter sets (physical dimensions, material properties,..)
Graph Based ML Modeling
  Metal traces in the EM structures are segmented to form graph representations
Image Based ML Modeling
  RF passive layouts are converted into layers of pixelated images representing metal or non-metal regions

## Slide 10: Tabular (or Template) Based ML Modeling
Parameterizes solenoidal inductor
Transposed-CNN model for across multiple frequencies
[Torun+, ICCAD’19]
[Sánchez-Masís+, LAMC’23]
Parameterizes PCB link between vias
Multi-layer perceptron (MLP) model for a frequency point
cavity height (h) | 9±3mils
pitch | 40±20mils
pad radius (pr) | 9.25±2.75mils
antipad radius (ar) | 14.75±4.25mils
loss tangent (δ) | {0.002, 0.02, 0.2}
plate thickness (t) | {1, 2}mils
stripline width (w) | 5.5± 1.5mils
distance between arrays (d) | 10.5±9.5cm
relative permittivity (εr) | 4.1 ±0.3
Notes: LAMC’23: A lot of work in package design that are like this work..
ICCAD19: Key contribution of this work is using the transposed-CNN model for the tabular input to predict S-parameter across multiple frequencies.
The transposed convolutional layers are introduced because the tabular inputs consist of a small number of parameters, but the output requires a higher dimensional representation..
So the transposed layer does something kind of opposite of conventional convolutional layer and expand the dimensionality.

## Slide 11: Graph Based ML Modeling
[Zhang+, ICML’19]
[Liu+, TCPMT’24]
[Kim+, DAC’24 ]
Represents 𝑁-resonator filter as graph
  Nodes : resonators (center coordinates, etc. )
  Edges: electromagnetic interaction between resonators
GNN model
Represents PCB interconnect (UCIe) as graph
  Nodes : each segmentation
  Edges: connection between segmentations
GNN model
Represents PCB interconnect as graph
Graph Transformer model

## Slide 12: Image Based ML Modeling
    Single-layer layout (pixelated to 18x18) for matching network
    Deep-CNN model
    Multi-layer layout (pixelated to 3x40x40) for generic impedance transformation network
    3D-to-2D UNet model
[Karahan+, JSSC’23]
[Chae+, ICCAD’24]
Notes: The most intuitive approach.
This approach enables the application of various image processing techniques in the AI field. Can leveraging data augmentation strategies

## Slide 13: ML Modeling: Challenges
Challenge: Representing solution space
  Tabular: Requires a predefined fixed set of template parameters
  Graph: Faces scalability issues as the trace segmentations increases
  Image: Demands significant computational resources
  Performance comparison is difficult
Challenge: Quality and quantity of the dataset
  Limited open datasets: NDA constraints from semiconductor foundries limits open-source RFIC datasets
  Costly dataset generation: Training datasets rely on expensive and time-consuming EM simulations

## Slide 14: ML Modeling: Future Directions
Current Key Contributions: Physics-augmented ML modeling
  Reduce data dependency by integrating physical knowledge with ML
  Causality Enforcement Layer :
  Passivity Enforcement Layer:
  Kramer-Kronig Compensation Layer:
Future Directions:
  Further exploration of methods to embed physical law into ML model
  Use of fast solvers with optimal complexity and transfer learning for technology-agnostic applications
  Development of open-source datasets
[Torun+, TMTT’20]
[Chae+, ICCAD’24]
Notes: Either embed a layer to be a part of ML architecture, or define training loss function to penalize when violated
Physics-augmented ML modeling shows promising result in successfully increasing model prediction accuracy and reducing the dataset required for model training.

## Slide 15: RFIC Passive Design Flow
Computationally expensive simulations
Iterative
Heuristically-constrained
High entry barriers for new designers
Fast evaluation utilizing ML models
Automated
Non-intuitive and beyond human
Lowered entry barriers for new designers

## Slide 16: Inverse Design Optimization
Quickly synthesize RF passive design to satisfy the given target performance
Tabular Design Space Optimization
Pixelated Design Space Optimization
Hybrid (template and pixelated) Design Space Optimization

## Slide 17: Tabular Design Space Optimization
Directly train ML model to predict the design parameters
  ML model is trained to do the “inverse” design
  Requires a strategy to resolve multi-modal output problem
[Er+, IMS’21]

## Slide 18: Pixelated Design Space Optimization
The entire design area is pixelated into bitmap of metal or non-metal
[Karahan+, JSSC’23]
[Lee+, NEWCAS’23]
[Karahan+, JSSC’23]

## Slide 19: Pixelated Design Space Optimization
Genetic Algorithm-based Optimization
[Karahan+, JSSC’23]
  Two best performing designs are selected from random set of designs
  Offsprings are reconstructed from each parent through a random cut line
  Random mutations on pixels are applied

## Slide 20: Hybrid Design Space Optimization
The design space is represented as the combination of conventional and pixelated approach
[Chae+, ICCAD’24]
28 parameters
Diverse ring shapes
Local deformations
Notes: This design space is inspired by the traditional ring structures seen in inductor, transformer and coupler structure.
Several parameters represent the diverse ring shape, allowing for more flexibility compared to traditional octagonal rings.
Moreover, we add more parameters to represent the local deformation in the width of the ring to expands the design space even more with non-intuitive choices.

## Slide 21: Hybrid Design Space Optimization
Bayesian Optimization
  Select new designs through probabilistic decision-making
  Optimize for ring-structure parameters
  Local deformations are treated as noise
Non-intuitive structure can achieve beyond template-based design
[Chae+, ICCAD’24]
Notes: The defined design space is then optimized with Bayesian optimization and probabilistic decision-making.
In this work, we specifically only optimized the design for ring structure parameters.
Introduced local deformations are treated as noise to the design to see if slight changes in the structure can lead to improved performance.
This is one of the highlighted result. You can see that the layout output of the framework is very not intuitive, and achieve the performance that cannot be achieved when relying on the predefined transformer behavior model in the manual design.

## Slide 22: Inverse Design: Challenges
Challenge: Design space definition
  Conventional tabular: highly restricted
  Complete pixelated: randomly scattered pixels and isolated shapes lead to redundant design performance
   Need to balance between exploitation and exploration of the design space
Solution:
  Hybrid-approach of flexible template-based with local deformations
Notes: Conventional tabular: highly restricted in design choices.
Complete pixelated approach: can unnecessary generate a very complex design space and also, the randomly scattered pixels can lead to redundant designs.

## Slide 23: Inverse Design: Future Direction
Future Directions:
  Incorporate RFIC domain knowledge to design space definition to ensure meaningful performance outcomes
  Introduce non-intuitive features to enhance flexibility
  Shift towards active-passive co-optimization, integrating both components into an end-to-end AI-assisted design flow
Active Device
Active
Optimization
Passive Network
Power
Amplifier
Passive
Optimization
Co-Optimization

## Slide 24: Conclusion
We have just scratched the surface of AI for RF IC design automation
Won’t replace experienced designers, but will replace “mundane” jobs, improve productivity, democratize RF IC designs (workforce development)
A lot of future research opportunities: incorporating physic laws, transfer learning, technology-agnostic applications, explanability, optimality, active-passive co-optimization,..
Notes: In summary, so far,….
Improve productivity, drive innovation and …

## Slide 25: NSTC 1st Jump Start R&D Program: AIDRFIC
UT Austin led project “GENIE-RFIC: Generative ENgine for Intelligent and Expedited RFIC Design” selected
We are hiring PhD students and postdocs (please contact Prof. David Pan)
Notes: Launched!

## Slide 26: Thank You